## Slide 1: Lecture # 3 (Final) Processor Logic Design (1st Part) ALU Design
Prof. Dr. Engr. Muhibul Haque Bhuyan
Professor
Department of Electrical and Electronic Engineering American International University Bangladesh (AIUB)

## Slide 2: Introduction
A processor unit is that part of a digital system that implements the operations in the system.
It comprises a number of registers and the digital functions that implement arithmetic, logic, shift, and transfer micro-operations.
The processor unit, when combined with a control unit that supervises the sequence of micro-operations, is called a central processing unit (CPU).
Central Processing Unit (CPU) consists of Memory (Register Banks), Arithmetic Logic Unit (ALU) and Control Unit (CU).
There are three organizations for organizing a general-purpose processor unit:
  Bus organization
  Scratchpad memory
  Two-port memory

## Slide 3: Bus Organization
Fig. 9.1 Processor registers and ALU connected through Common Buses
A bus organization has 4 registers, each register is connected to 2 multiplexers to form 2 buses A and B.
To perform the micro-operation:
  R1 = R2 + R3
The control unit must provide binary selection variables to the following selector inputs –
MUX A Selector: to place contents of R2 onto bus A
MUX B Selector: to place contents of R3 onto bus B
ALU Function Selector: to provide the arithmetic operation A + B
Shift Selector: for direct transfer from the output of the ALU onto output bus S (no shift)
Decoder Destination Selector: to transfer the contents of bus S into R1

## Slide 4: Bus Organization
The five control selection variables must be generated simultaneously and must be available during one common clock pulse interval.
The binary information from two source registers propagates through the combinational gates in the multiplexers, the ALU, and the shifter, to the output bus and into the inputs of the destination register all during one clock pulse interval.
Then, when the next clock pulse arrives, the binary information on the output bus is transferred to R1.

## Slide 5: Scratchpad Memory
The registers in a processor unit can be enclosed within a small memory unit. When included in a processor unit, a small memory is sometimes called a scratchpad memory.
The use of a small memory is a cheaper alternative to connecting processor registers through a bus system. The difference between the two systems is the manner in which information is selected for transfer into the ALU.
In the bus system, the information transfer is selected by the multiplexers that form the buses.
On the other hand, a single register in a group of registers organized as a small memory must be selected by means of an address to the memory unit.

## Slide 6: Scratchpad Memory
To perform the operation R1 = R2 + R3, the control must provide binary selection variables to perform the following sequence of three microoperations:
  T1: A  M[010] Read R2 into register A
  T2: B  M[011] Read R3 into register B
  T3: M [001]  A+B Perform the operation in ALU and transfer the result to R1
The reason for a sequence of 3 microoperations, instead of just 1 as in a bus-organized processor, is due to the limitation of the memory unit having only one set of address terminals but two source registers are to be accessed. So, multiple memory addresses can’t be accessed simultaneously.
Fig. 9.2 Processor unit employing a scratchpad memory

## Slide 7: Processor Unit with 2-Port Memory
Some processors employ a 2-port memory to overcome the delay caused when reading two source registers.
If the destination register is the same as one of the source registers, then the entire micro-operations can be done within one clock pulse period.
Fig. 9.3 Processor unit with a 2-port memory

## Slide 8: Processor Unit with 2-Port Memory
When CP = 1, A and B latches are open and accept information coming from memory. The WE is also in a HIGH state and disables write operation and enables read operation. Thus, when CP = 1, words selected by A and B addresses are read from memory and placed in A and B registers.
When CP = 0, the latches are closed and retain the last data entered. ALU operation is performed and if a write is enabled since CP = 0, and also ME input is enabled, the result of the micro-operation is written into memory word defined by B address.
Fig. 9.3 Processor unit with a 2-port memory
=1
1

## Slide 9: Arithmetic Logic Unit (ALU)
An Arithmetic Logic Unit (ALU) is a multi-operation, combinational logic digital functional circuit.
The ALU can perform a set of basic arithmetic and logic operations.
The ALU has several selection lines to select a particular operation in the unit.
The selection lines are decoded within the ALU so that k selection variables can specify up to distinct operations.

## Slide 10: Arithmetic Logic Unit (ALU)
The mode select s2 distinguishes between arithmetic and logic operations.
The two function-select inputs s1 and s0 specify the arithmetic and logic operation to be generated.
The input and output carry (Cin and Cout) have meanings only during arithmetic operations.
The input carry Cin in the least significant position of an ALU is quite often used as the fourth selection variable that can double the number of arithmetic operations. Thus, a total of 8 arithmetic operations and 4 logical operations can be performed.

## Slide 11: Design of Arithmetic Circuit
The basic component of the arithmetic section of an ALU is the parallel adder.
A parallel adder is constructed with several full adder circuits cascaded.
By controlling the data inputs to the parallel adder, it is possible to obtain different types of arithmetic operations.

## Slide 12: Operations obtained by controlling one set of inputs to a parallel adder
= 01
Fig. 9.6
(a) Addition without input carry
(b) Addition with input carry
(c) Addition with 1’s complement of B
(d) Subtraction
= 10

## Slide 13: Operations obtained by controlling one set of inputs to a parallel adder
= 00
Fig. 9.6
(e) Transfer of A
(f) Increment of A
(g) Decrement of A
(h) Transfer of A
= 11

## Slide 14
The condition illustrated in Fig. 9.6 (g) inserts all 1s into the B terminals. This produces the decrement operation, F = A – 1. To show that this condition is indeed a decrement operation, consider a parallel adder with n full-adder circuits. When the output carry is 1, it represents the number 2n because 2n in binary consists of a 1 followed by n 0s. Subtracting 1 from 2n, we obtain 2n – 1, which in binary is a number of n 1s. Adding 2n – 1 to A, we obtain F = A + 2n – 1 = 2n + A – 1. If the output carry 2n is removed then we obtain the decrement operation, F = A – 1.
To demonstrate with a numerical example, let us consider, n = 8 and A = 9. Then
A = 0000 1001 = 9
28 = 1 0000 0000 = 256
28 – 1 = 1111 1111 = 255
A + 28 – 1 = 1 0000 1000 = 256 + 8
Removing the output carry 2n = 256, we obtain 8 (i.e., 9 – 1). Thus, we have decremented A by 1 (from 9 to 8) by adding to it a binary number with all 1s.

## Slide 15: Function Table for Arithmetic Circuit
Table 9.1 Function Table for the arithmetic circuit of Fig. 9.8

## Slide 16: Functions of Arithmetic Circuit
The circuit that controls input B to provide the functions illustrated in Fig. 9.6 is called a true/complement, one/zero element. The circuit is illustrated in Fig. 9.7.
Two selection lines s1 and s0 control the input of each B terminal. The diagram shows one typical input designated by Bi and an output designated by Yi.
In a typical application, there are n such circuits for i = 1, 2, 3, ……, n.
As shown in the Table of Fig. 9.7, when both s1 and s0 are equal to zero, the output Yi is equal to 0 regardless of the value of Bi.
When s1 = 0 and s0 = 1, the top AND gate generates the value of Bi while the bottom AND gate output is 0; thus, the output Yi is equal to Bi.
With s1 = 1 and s0 = 0, the bottom AND gate generates the complemented value of Bi while the top AND gate output is 0; thus, the output Yi is equal to B’i.
Finally, when both s1 = 1 and s0 = 1, both the top and bottom AND gates generate the normal and complemented value of Bi respectively; thus, the output Yi is equal to Bi + Bi’, which is equal to 1.
These are illustrated in the Table of Fig. 9.7

## Slide 17: True/Complement, One/Zero Circuit
The values of the Y inputs to the full-adder circuits are a function of selection variables and .
Fig. 9.7 True/complement, one/zero element
The arithmetic circuit needs a combinational circuit in each stage specified by Boolean functions –
Xi = Ai
Yi = Bis0 + Bi’s1 , i= 1,2,3,...,n
0 | 0 | 0
0 | 1 | Bi
1 | 0 | Bi’
1 | 1 | 1
0 | 0 | 0
0 | 1 | Bi
1 | 0 | Bi’
1 | 1 | 1

## Slide 18: Logic Diagram of an Arithmetic Circuit
Figure 9-8 Logic Diagram of a 4-bit Arithmetic Circuit

## Slide 19: Exercise (Homework)
Design an adder/subtractor circuit with one selection variable s and two inputs A and B: when s = 0 the circuit performs A+B. When s = 1 the circuit performs A-B by taking the 2’s complement of B.
Xi = Ai
Yi = Bi XOR s
Cin = s
s | F | X | Y | Cin
0 | A+B | A | B | 0
1 | A-B | A | B’ | 1
Truth Table of XOR gate

## Slide 20: Design of a Logic Circuit
The logic microoperations manipulate the bits of the operands separately and treat each bit as a binary variable.
All logic operations can be obtained by means of AND, OR and NOT operations.
For 3 operations, we need 2 selection variables but 2 selection lines can choose between 4 logic operations and hence XOR operation was also incorporated in the logical circuit.

## Slide 21: Combining Logic and Arithmetic Circuits
The logic circuit can be combined with the arithmetic circuit to produce one arithmetic logic unit.
Selection variables s1 and s0 can be made common to both sections provided we use a third variable s2 to differentiate between the two.
This third variable is the select input to a 2:1 multiplexer.

## Slide 22: Logic Operations in One Stage of Arithmetic Circuit
Table 9-3 Logic operations in one state of arithmetic circuit
?
?
XNOR gate gives an output “1” when its inputs are “logically equal” or “equivalent” to each other, which is why an Exclusive-NOR gate is sometimes called an Equivalence Gate.
Input |  | Output
A | B | A XNOR B
1 | 0 | 0
1 | 1 | 1

## Slide 23: Problems of combining the Arithmetic and Logic Circuits in one stage
The value of Xi is always equal to input Ai. Table 9.3 shows the four logic operations obtained when a third selection variable s2 = 1. This selection variable forces Ci to be equal to 0 while s1 and s0 choose a particular value for Yi.
The four logic operations obtained by this configuration are transfer, exclusive OR (XOR), equivalence (XNOR), and complement. The third entry is the XNOR operation because of the following-
The last entry in the table is the NOT or complement operation because of the following-

## Slide 24: Design of Arithmetic Logic Unit
The design steps of an ALU are as follows:
Design an arithmetic section independent of the logic section
Determine the logic operations obtained from the arithmetic circuit in step 1, assuming the input carries of all stages are 0.
Modify the arithmetic circuit to obtain the required logic operation

## Slide 25: Logic Diagram of an Arithmetic Circuit
Table 9-3
?
?
Figure 9-8 Logic Diagram of a 4-bit Arithmetic Circuit

## Slide 26: Converting an Arithmetic Circuit to Logic Circuit
The solution to the first design step is shown in Fig. 9.8. The solution to the second design step is presented in Table 9.3. The solution of the third step is shown below.
From Table 9.3, we see that when s2 = 1, the input carry Ci in each stage must be 0. When both s1 and s0 are equal to 0, each stage generates the output function Fi = Ai. To change the output to an OR operation, we must change the input to each full-adder circuit from Ai to Ai + Bi. This can be accomplished by ORing Ai and Bi when s2s1s0 = 100.
The other selection variable combinations that gives an undesirable output is s2s1s0 = 110. The present unit generates the output, as discussed in the previous slide. However, we want to generate the AND operation (i.e., ) for this combination. For this purpose, let us investigate the possibility of ORing each input Ai with a Boolean variable Ki. The function so obtained is used for Xi when s2s1s0 = 110.

## Slide 27: Converting an Arithmetic Circuit to Logic Circuit
If the value of Ki is ORed with input Ai then we obtain (remember, when s2s1s0 = 110 then and ),
Careful inspection of the result reveals that if the variable is replaced by then the second and third terms will be eliminated from the final expression above, because and thus we get the required AND operation between A and B.
Therefore, we conclude that to get the required AND operation, we must make an OR operation between and before applying it to the input of the full-adder circuit when s2s1s0 = 110 and input of the full-adder circuit will get .

## Slide 28: Converting an Arithmetic Circuit to Logic Circuit
The final ALU is shown in Fig. 9.13. Only the first two stages are drawn, but the diagram can be easily extended to more stages. The inputs to each full-adder circuit are specified by the Boolean functions:
When then these three function reduce to-
These are the functions of the arithmetic circuit of Fig. 9.8

## Slide 29: Converting an Arithmetic Circuit to Logic Circuit
When then these three function reduce to-
These are the functions of the logic circuit of Fig. 9.8.
When s2s1s0 = 100, and Hence, we can get the OR operation at the output, .
When s2s1s0 = 101, and Hence, we can get the required XOR operation at the output, .

## Slide 30: Converting an Arithmetic Circuit to Logic Circuit
When then these three function reduce to-
These are the functions of the logic circuit of Fig. 9.8.
When s2s1s0 = 110, and Hence, we can get the required AND operation at the output, .
When s2s1s0 = 111, and Hence, we can get the required NOT operation at the output, .

## Slide 31: Logic Diagram of ALU (Only the first two stages are drawn)
Figure 9.13: Logic diagram of ALU
Converting an Arithmetic Circuit to Logic Circuit
Table 9-3
?
?

## Slide 32: Converting an Arithmetic Circuit to Logic Circuit
The 12 operations (8 arithmetic and 4 logical) generated in the ALU are summarized in Table 9.4. The function is selected through s2, s1, s0, and Cin.
The arithmetic operations are identical to the ones listed for the arithmetic circuit. The value of Cin for the four logic functions has no effect on the operations of the unit and those entries are marked as don’t cares (Xs).
Table 9.4

## Slide 33: Design of Arithmetic Logic Circuit [Supplement Starts]
Design a 2-bit ALU for the operations listed below in the Table:
Binary Code |  |  | Function of selection variables |  |  | 
 | B | A | F with Cin = 0 | F with Cin = 1 | D | H
0 0 0 | Input Data | Input Data | A | A+1 | None | Circulate-Left with Carry
0 0 1 | R1 | R1 | A+B | A+B+1 | R1 | Circulate-Right with Carry
0 1 0 | R2 | R2 | A+B` | A+B`+1 | R2 | No shift
0 1 1 | R3 | R3 | A-1 | A | R3 | 0’s to the output Bus
1 0 0 | R4 | R4 | A OR B | A OR B | R4 | -
1 0 1 | R5 | R5 | A XOR B | A XOR B | R5 | Shift Left with IL=0
1 1 0 | R6 | R6 | A AND B | A AND B | R6 | Shift Right with IR=0
1 1 1 | R7 | R7 | A′ | A′ | R7 | 1’s to the output Bus

## Slide 34: Design of Arithmetic Logic Circuit
Xi | Yi | Zi
A | 0 | 0
A | 0 | 1
A | B | 0
A | B | 1
A | B’ | 0
A | B’ | 1
A | 1 | 0
A | 1 | 1
A+B | 0 | 0
A | B | 0
A+B’ | B’ | 0
A | 1 | 0

## Slide 35: Design of Arithmetic Logic Circuit (K-maps)
S0 S2S1 | 0 | 1
00 | A | A
01 | A | A
11 | A+B’ | A
10 | A+B | A
S0 S2S1 | 0 | 1
00 | 0 | B
01 | B’ | 1
11 | B’ | 1
10 | 0 | B
S0Cin S2S1 | 00 | 01 | 11 | 10
00 | 0 | 1 | 1 | 0
01 | 0 | 1 | 1 | 0
11 | 0 | 0 | 0 | 0
10 | 0 | 0 | 0 | 0
For an arithmetic circuit, we don’t need to change A for X, but for a logic circuit, we need to change A and we don’t need Cin. So, we need to use only three variables (s2, s1, and s0) in the K-map.
For both arithmetic and logic circuits, we need to change B for Y for the same combination of s2, s1, and s0, but for a logic circuit, we don’t need Cin. So, we need to use only 3 variables (s2, s1, and s0) in the K-map.
For the arithmetic circuit, we need Cin for all combinations of s2, s1, and s0, but for a logic circuit, we don’t need Cin. So, we need to use all 4 variables (s2, s1, s0, and Cin) in the K-map to force Cin to zero for Z for the same combination of s2, s1, and s0.

## Slide 36: Design of Arithmetic Logic Circuit
Figure 9.13: Logic diagram of arithmetic logic circuit

## Slide 37: Next Class…..
Status Register
Shifter
Design of a processor unit with control variables
Micro operations for processor

## Slide 38: Thanks for attending….
?