## Slide 1: Lecture -1 Sequential Circuit Design Latches and Flip-Flops

## Slide 2
Latches
A latch is a temporary storage device that has two stable states (bi-stable).
It is a basic form of temporary storage device which can reside in either 1 or 0.
The S-R (Set-Reset) latch is the most basic type.
It can be constructed from two cross-coupled NOR gates or NAND gates.
With NOR gates the latch responds to active-HIGH inputs.
With NAND gates the latch responds to active-LOW inputs.
An Active-HIGH S-R Latch
An Active-LOW S-R Latch

## Slide 3
Latches
Block diagram of an Active-HIGH S-R Latch
For an Active-HIGH S-R Latch there are no bubbles in the inputs.
Block diagram of an Active-LOW S-R Latch
For an Active-LOW S-R Latch there are bubbles in the inputs.

## Slide 4
Latches
Operation of an Active-HIGH S-R Latch
STARTING CONDITION Q=0 AND =1
WHEN S=1, R=0, Q=0 AND =1 (SET OPERATION)
  =0. AS =0 AND R=0, Q=1.
WHEN S=0, R=0, Q=1 AND =0 (MEMORY OPERATION)
  AS S=0 AND Q=1, =0.
  AS =0 AND R=0, Q=1.
WHEN S=0, R=1, Q=1 AND =0 (RESET OPERATION)
  AS R=1, Q=0.
  AS Q=0 AND S=0, =1
When both inputs are 1, the operation is INVALID
Truth-table for NOR gate

## Slide 5
Latches
Table of operation of an Active-HIGH S-R Latch

## Slide 6
Latches
Operation of an Active-LOW S-R Latch
STARTING CONDITION Q=0 AND =1
WHEN S=0, R=1, Q=0 AND =1 (SET OPERATION)
  Q=1. AS Q=1 AND R=1, =0.
WHEN S=1, R=1, Q=1 AND =0 (MEMORY OPERATION)
  AS S=1 AND =0, Q=1.
  AS Q=1 AND R=1, =0.
WHEN S=1, R=0, Q=1 AND =0 (RESET OPERATION)
  AS R=0, =1.
  AS =1 AND S=1, Q=0
When both inputs are 0, the operation is INVALID
Truth-table for NAND gate

## Slide 7
Latches
Table of operation of an Active-LOW S-R Latch

## Slide 8
Latches
Exercise 1:
SOLUTION

## Slide 9
Gated S-R Latches
A gated latch is a variation of basic latch.
A gated latch has an extra input “ENABLE” (EN).
The latch responds to S and R if and only if EN is HIGH.
So the extra input brings more control over the operation.
Gated Latches are level sensitive.
A gated S-R Latch
Block diagram of a gated S-R Latch

## Slide 10
Gated S-R Latches
Table of operation for a gated S-R Latch
Logic Circuit of a gated S-R Latch
Truth table for a NAND gate

## Slide 11
Gated S-R Latches
Exercise 2:
SOLUTION

## Slide 12
Gated D Latches
The D latch is another variant of latches
It combines the S and R input into a single input D.
When D and EN is HIGH, the latch is SET.
When D is LOW and EN is HIGH, the latch is RESET.
A simple rule is, when EN is HIGH, the Q follows the input D
A gated D-Latch
Block diagram of a gated D-Latch

## Slide 13
Gated D Latches
Logic Circuit of a Gated D-Latch
Table of operation for Gated D-Latch

## Slide 14
Exercise 3:
Gated D Latches
SOLUTION

## Slide 15
Flip-Flops
Flip-Flops are synchronous bi-stable devices, also know as bi-stable multi-vibrator.
Synchronous means the output changes only at the triggering of a control input “Clock”.
Compared to gated latches, flip-flops are edge triggered devices.
Edge triggered means, the output only changes at “Rising Edge” or “Falling Edge” of a clock.
A rising edge triggered device is also called a positive edge triggered device.
A falling edge triggered device is also called a negative edge triggered device.
a) D Flip-Flop
b) J-K Flip-Flop
a) D Flip-Flop
b) J-K Flip-Flop
Positive edge triggered Flip-Flops
Negative edge triggered Flip-Flops

## Slide 16
D Flip-Flops
Positive edge triggered D-flip flop
Negative edge triggered D-flip flop
The D input is a synchronous input, as the input is only transferred at the triggering of a clock pulse (positive or negative).
The operation is almost similar to that of a D latch.
At a clock pulse, if D is HIGH, the flip-flop is SET, so and .
At a clock pulse, if D is LOW, the flip-flop is SET, so and .

## Slide 17
D Flip-Flops
b) Positive edge triggered D flip-flop
a) Operation table of positive edge triggered D flip-flop
In the operation table, the arrow indicates the rising edge, and thus it is a positive edge triggered D flip-flop.
Rising edge is indicated by an upward arrow, likewise, a falling edge is indicated by a downward value.
The circuit diagram of a D flip-flop is also similar to a gated D Latch, except for an additional pulse transition detector.
The pulse transition detector is used to produce the triggering edge.

## Slide 18
D Flip-Flops
SOLUTION
Exercise 4:

## Slide 19
JK Flip-Flops
Block diagram of positive-edge triggered J-K flip-flop
Logic circuit of positive-edge triggered J-K flip-flop
The JK Flip-Flop is a more versatile and widely used type of Flip-Flop.
The J and K inputs are synchronous inputs.
The JK flip-flop eradicates the problem of SR flip-flop.
JK flip-flops does not have the invalid state.
When both J and K are HIGH, a JK flip-flop performs the toggle operation.
JK flip-flops are widely used to make counters.

## Slide 20
Characteristic table of positive-edge triggered J-K flip-flop
JK Flip-Flops
Set Operation
Reset Operation
Toggle Operation
Memory Operation

## Slide 21
JK Flip-Flops
SOLUTION
Exercise 5:

## Slide 22
JK Flip-Flops with Asynchronous Inputs
Most flip-flops also have asynchronous inputs other than their synchronous inputs.
The asynchronous inputs affect the output independent of the presence of clock edge.
Two such inputs are Preset and Clear.
Both are Active-LOW, that is, they affect the output when they are LOW.
When Preset is LOW, it sets the flip-flop, irrespective of the synchronous inputs.
When Clear is LOW, it resets the flip-flop, irrespective of the synchronous inputs.

## Slide 23
JK Flip-Flops with Asynchronous Inputs
Exercise 6:
SOLUTION

## Slide 24
Application of Flip-Flops
DATA STORAGE
D flip-flops can be used as parallel data storage devices.
Multiple D flip-flops are connected in parallel.
For a N-bit data, N no. of flip-flops are required.
The data is stored at the triggering edge of the clock pulse.
Figure shows a 4-bit positive edge triggered data storage device.
The same clock is parallel connected to all the flip-flops.
The input of the flip-flops are connected to the data bus.
At every clock pulse, the data in the data bus gets stored in the flip-flops.
The device also has common asynchronous Clear input.
When the memory is needed to emptied, the Clear input is set to LOW.

## Slide 25
Application of Flip-Flops
FREQUENCY DIVISION
JK flip-flops can be used to slow down clocks.
It is also known as frequency division.
The JK flip-flop is operated in the toggle mode.
Each flip-flop divides the frequency by 2.
There fore, N flip-flops can be connected in series to divide the frequency by 2N.
A benefit of using flip-flops for frequency division is that the duty cycle is exactly 50%.
The figure shows the arrangement to divide the clock frequency by 4.

## Slide 26
Application of Flip-Flops

## Slide 27
Application of Flip-Flops
COUNTING
Flip-flops can also be used to make digital counters.
JK flip-flops are used to make counters.
JK flip-flop is operated in the toggle mode.
N flip-flops are required for N-bit counters.
Counters can be synchronous or asynchronous.

## Slide 28
References
Thomas L. Floyd, “Digital Fundamentals” 11th edition, Prentice Hall – Pearson Education.
Thank You