## Slide 1: IP Addressing- I
Course Code: CSC 3116
Dept. of Computer Science
Faculty of Science and Technology
Course Title: Computer Networks
Lecturer No: | Lab 1 | Week No: | 1 | Semester: | Summer 23-24
Lecturer: | Md. Faruk Abdullah Al Sohan; faruk.sohan@aiub.edu |  |  |  | 

## Slide 2: Lecture Outline
Classification of Address
Conversion from binary to decimal and vice-versa
Range of Address

## Slide 3: How to identify the recipient?

## Slide 4: How to identify the recipient? (contd…)
Sender
Receiver
Is single address
enough for both LAN
and collection of
networks?

## Slide 5: Classification of Address
Address
  Physical Address
  Logical Address
  Port Address

## Slide 6: Physical Address
The address of a node as defined by its LAN
The lowest-level address
The size and format of these addresses vary depending on the network
Ethernet uses 6 bytes address (imprinted on Network Interface Card (NIC)

## Slide 7: Physical Address (contd…)
6-byte address is also called Medium Access Control (MAC) address
No two NICs ever share the same MAC address
Either imprinted on the surface or burnt into a ROM chip
CA1885-0CB72C
CA-18-85-0C-B7-2C
Organizationally
Unique Identifier
Device ID
Network Interface Card

## Slide 8: Physical Address (contd…)

## Slide 9: Physical Address (contd…)
Use of Physical Address

## Slide 10: Logical Address
  Physical address is not suitable for internetwork as different networks can have different address formats
  A universal addressing system is needed in which each host can be identified uniquely, regardless of the underlying physical network
  Can be changed depending on the network
  No two publicly addressed and visible hosts on the Internet can have the same logical address (widely known as Internet Protocol (IP) address.
  32-bits length

## Slide 11: Port Address
  Used to identify a process (Email, FTP)
  16-bits length
  Internet Assigned Number Authority (IANA) assigns Port address

## Slide 12: Port Address

## Slide 13: Binary-to-Decimal Conversion
For addressing, we require
to convert a 8-bits binary to decimal
To convert a decimal number of up to 255 to binary number
Digit | x8 | x7 | x6 | x5 | x4 | x3 | x2 | x1
Position of digit, i | 8 | 7 | 6 | 5 | 4 | 3 | 2 | 1
Contribution of the digit, 2i-1 | 28-1 | 27-1 | 26-1 | 25-1 | 24-1 | 23-1 | 22-1 | 21-1
Decimal contribution | 128 | 64 | 32 | 16 | 8 | 4 | 2 | 1

## Slide 14: Binary-to-Decimal Conversion
Digits | 1 | 0 | 0 | 1 | 1 | 0 | 0 | 1
Position | 8 | 7 | 6 | 5 | 4 | 3 | 2 | 1
Contribution | 128 |  |  | 16 | 8 |  |  | 1
128+16+8+1=153
(10011001)2=(153)10

## Slide 15: Binary-to-Decimal Conversion
0 | 1 | 0 | 0 | 1 | 1 | 0 | 1
Digits | 0 | 1 | 0 | 0 | 1 | 1 | 0 | 1
Position | 8 | 7 | 6 | 5 | 4 | 3 | 2 | 1
Contribution |  | 64 |  |  | 8 | 4 |  | 1
64+8+4+1=77
(01001101)2=(77)10

## Slide 16: Decimal-to-Binary Conversion
(172)10 =( )2
(172)10 =( 10101100)2

## Slide 17: Decimal-to-Binary Conversion
(20)10 =( )2
(20)10 =( 00010100)2

## Slide 18: Decimal-to-Binary Conversion
Convert the following:
210, 50, 65, 172, 169
11001010, 11100001, 10101111

## Slide 19: IP Address
IP=Internet Protocol
Unique and universal
32-bit binary address
Divided into four octate
Octets are separated by dot (.) sign
10000000000010110000001100011111
10000000 00001011 00000011 00011111
Octet
10000000.00001011.00000011.00011111
IP Address
Doted Decimal of IP address
128.11.3.31
Address space
Total number of address used by a protocol
For b bits, the address space is 2b

## Slide 20: IP Address
Example
Example

## Slide 21: IP Address
192.168.10.25
16.32.25.31
78.123.222.44
11110000.10101010.11100011.00011100
10001000.10010011.11100000.00000110
Example
Example

## Slide 22: IP Address
Example

## Slide 23: Ranges of Address
Example
Solution
Example
Solution

## Slide 24
References
  1. Official Cert Guide CCNA 200-301 , vol. 1, W. Odom, Cisco Press, First Edition, 2019, USA.
  2. CCNA Routing and Switching, T. Lammle, John Wily & Sons, Second Edition, 2016, USA.
  3. Cisco IOS Configuration Fundamentals Command Reference.
  http://www.cisco.com

## Slide 25
Books
  1. Official Cert Guide CCNA 200-301 , vol. 1, W. Odom, Cisco Press, First Edition, 2019, USA.
  2. CCNA Routing and Switching, T. Lammle, John Wily & Sons, Second Edition, 2016, USA.