## Slide 1: Transport Layer Protocols II
Course Code: COE 3206
Dept. of Computer Science
Faculty of Science and Technology
Course Title: Computer Networks
Lecturer No: | 14 | Week No: | 15 | Semester: | Summer 23-24
Lecturer: | Md. Faruk Abdullah Al Sohan; faruk.sohan@aiub.edu |  |  |  | 

## Slide 2: Lecture Outline
Congestion in networks
Congestion control
  TCP Reno
Error control principle
  Sliding window technique

## Slide 3: Congestion in networks
Congestion
Congestion is a situation in a network in which the load on the network, the number of packets sent to the network, is greater than the capacity of the network, the number of packets a network can handle.
Congestion control
Congestion control refers to the mechanisms and techniques to control the congestion and keep the load below the capacity [1].

## Slide 4: Congestion in networks…
Congestion in a network or internetwork occurs because routers and switches have queues-buffers that hold the packets before and after processing.
A router, for example, has an input queue and an output queue for each interface.
When a packet arrives at the incoming interface, it undergoes three steps before departing:
The packet is put at the end of the input queue while waiting to be checked.
The processing module of the router removes the packet from the input queue once it reaches the front of the queue and uses its routing table and the destination address to find the route.
The packet is put in the appropriate output queue and waits its turn to be sent.

## Slide 5: Congestion in networks…
Two possible scenarios in a router:
  Packet arrival rate > packet processing rate,
  the input queues become longer and longer.
  2. Packet departure rate < Packet processing rate,
  the output queues become longer and longer

## Slide 6: Congestion Control
Terminology
Congestion Window
  The number of bytes the sender may have in the network at any time [2]
  LastByteSent – LastByteAcked <= cwnd
Sending Rate
  The congestion window size divided by the round-trip time (RTT1) of the connection [2].
By adjusting the value of cwnd, the sender can therefore adjust the rate at which it sends data into its connection [3].
1 The time from when a segment is sent until it is acknowledged.

## Slide 7: Congestion Control
Terminology
Loss Event
  Timeout
    Sender does not receive any acknowledgement within a predefined interval
  3 duplicate Acknowledgement (3 duplicate ACK)
    Reception of the same ACK four times.
    Indicates that the channel is not congested that much
    as the receiver is still receiving segments.
    Indicates that the segment 3 is lost as it receives the duplicate
    ACK 3
    Receiver is receiving segment out of order.
ACK 2
ACK 3
ACK 3
ACK 3
ACK 7
ACK 3

## Slide 8: Congestion Control
TCP Reno
Steps of congestion window control
  Slow Start
  Congestion Avoidance

## Slide 9: Congestion Control
TCP Reno
Slow Start
  Follows a greedy approach.
  Starts sending data of size equals maximum sized segment (MSS).
  If it receives an ACK for the previous transmission by next RTT  it sends 2 MSS.
  After next RTT, if it receives two ACKs  it sends 2+2=4 MSS in next round.
Fig. 1 Slow start from an initial congestion
window of one segment [2].

## Slide 10: Congestion Control
TCP Reno
Slow Start (cont.)
  That is, in each round, N+M MSS in a round if it sends N MSS in the last transmission round and receives M ACK before the current round.
  If it receives ACK for all the N MSS (previously sent), it sends N+N MSS this round.
Fig. 1. Slow start from an initial congestion
window of one segment [2].

## Slide 11: Congestion Control
TCP Reno
Congestion Avoidance
  How long does cwnd continue to be increased exponentially?
Increase cwnd by1 per transmission round
That is, increase cwnd linearly1
1. Usually timeout and 3 duplicate ACK do not happen in slow start
Fig. 2. Linear increase of cwnd

## Slide 12: Congestion Control
TCP Reno
  How long does cwnd continue to be increased linearly?
Until one of two incidents happen
  Timeout
  3 duplicate ACK
  Timeout
Start slow start
Timeout
Threshold
Fig. 3. Timeout

## Slide 13: Congestion Control
TCP Reno
  3 duplicate ACK
Start congestion avoidance
Fig. 4. 3 duplicate ACK
RTT
cwnd
3-duplicate ACK
ssth
ssth

## Slide 14: Congestion Control
TCP Reno
Fig. 5. TCP reno example

## Slide 15
Find the Events in the TCP RENO. What are The Values Of Ssthresh And Cwnd at Each Event.

## Slide 16: Task 2
Identify Timeout/3 duplicate ACK incidence. Also identify slow start, congestion avoidance period.

## Slide 17: Flow control
The TCP stores the data that needs to be sent in the send buffer and the data to be received in the receive buffer. Flow control makes sure that no more packets are sent by the sender once the receiver’s buffer is full as the messages will be dropped and the receiver won’t be able to handle them. In order to control the amount of data sent by the TCP, the receiver will create a buffer which is also known as Receive Window.

## Slide 18: Flow control
Send window
  Sequence of byte numbers of which some are sent but yet to be acknowledged
  while others are waiting to be sent
  Maintained by sender
Receive window
  Sequence of byte numbers which are expected to be received
  Maintained by receiver

## Slide 19
References
[1] B. A. Forouzan, Data Communication and Networking, 4th ed., Tata McGraw Hill Companies, Inc., New Delhi, 2010, pp. 385.
[2] A. S. Tanenbaum and D. J. Wetherall, Computer Networks, 5th ed., Pearson
Education India, 2013, pp. 571-572.
[3] J. F., Kurose and K. W. Ross, Computer Networking: A Top-Down Approach, 7th ed.,
Pearson Education, Inc., USA, 2017, pp. 274-277.
[4] D. Medhi and K. Ramassamy, Network Routing Algorithms, Protocols and
Archtectures, 2nd ed., Elsevier Inc., 2018, pp. 607-608.
[5] D. Runemalm , D. M. Sarwar and M. Shalbaf, “Decreasing the Hybrid-ARQ bandwidth
overhead through the Multiple Packet NAK (MPN) protocol”,
https://www.researchgate.net/publication/267554658 , [Accessed: April. 22, 2020].
[6] B. A. Forouzan, TCP/IP Protocol Suite, 4th ed., McGraw Hill Companies, Inc., USA,
2010, pp. 457-462.

## Slide 20
Recommended Books
  Data Communications and Networking, B. A. Forouzan, McGraw-Hill, Inc., Fourth Edition, 2007, USA.
  Computer Networking: A Top-Down Approach, J. F., Kurose, K. W. Ross, Pearson Education, Inc., Sixth Edition, USA.
  Official Cert Guide CCNA 200-301 , vol. 1, W. Odom, Cisco Press, First Edition, 2019, USA.
  CCNA Routing and Switching, T. Lammle, John Wily & Sons, Second Edition, 2016, USA.
  TCP/IP Protocol Suite, B. A. Forouzan, McGraw-Hill, Inc., Fourth Edition, 2009, USA.
  Data and Computer Communication, W. Stallings, Pearson Education, Inc., Tenth Education, 2013, USA.