## Slide 1: Chapter 1: Introduction to Personal Computer Hardware
Instructor Materials
IT Essentials 7.0
Click to add text
Notes: Cisco Networking Academy Program
IT Essentials 7.0
Chapter 1: Introduction to Personal Computer Hardware

## Slide 2: Instructor Materials – Chapter 1 Planning Guide
This PowerPoint deck is divided in two parts:
Instructor Planning Guide
  Information to help you become familiar with the chapter
  Teaching aids
Instructor Class Presentation
  Optional slides that you can use in the classroom
  Begins on slide # 13
Note: Remove the Planning Guide from this presentation before sharing with anyone.
Notes: 2

## Slide 3: Chapter 1: Introduction to Personal Computer Hardware
IT Essentials 7.0 Planning Guide
Notes: Cisco Networking Academy Program
IT Essentials 7.0
Chapter 1: Introduction to Personal Computer Hardware

## Slide 4: Check Your Understanding and What Do You Already Know?
Check Your Understanding activities used to be called Interactive Activities. They simply have a new name. They are designed to let students quickly determine if they understand the content and can proceed, or if they need to review.
Check Your Understanding activities do not affect student grades.
Activities listed as What Do You Already Know? are a type of activity in which we ask the student to simply take a guess! It is not meant to evaluate their knowledge. It is only meant to give them a head start in thinking about different topics before they are presented in the course. Students receive addition content in the form of feedback for any answers they select.
What Do You Already Know? activities do not directly affect student grades; however, the feedback may contain content which appears later in quizzes and exams, so it is important that students complete the What Do You Already Know? activities.
There are no separate slides for these activities in the PPT. They are listed in the notes area of the slide that appears before these activities.
Notes: 4

## Slide 5: Chapter 1: Activities
What activities are associated with this chapter?
Page # | Activity Type | Activity Name | Optional?
1.1.1.1 | Video Explanation | What is in a computer? | Recommended
1.1.2.3 | Check Your Understanding | ESD Characteristics | Recommended
1.2.1.5 | Check Your Understanding | Cases and Power Supplies | Recommended
1.2.2.5 | Check Your Understanding | Motherboards | Recommended
1.2.3.3 | Check Your Understanding | CPUs and Cooling Systems | Recommended
1.2.4.5 | Check Your Understanding | Memory | Recommended
1.2.5.2 | Check Your Understanding | Adapter Cards and Expansion Slots | Recommended
1.2.6.5 | Check Your Understanding | Data Storage Devices | Recommended
Notes: 5

## Slide 6: Chapter 1: Activities (Cont.)
What activities are associated with this chapter?
Page # | Activity Type | Activity Name | Optional?
1.2.7.2 | Check Your Understanding | Types of Optical Media | Recommended
1.2.8.4 | Check Your Understanding | Cables and Connectors | Recommended
1.2.9.5 | Check Your Understanding | Input Devices | Recommended
1.2.10.6 | Check Your Understanding | Identify Visual and Auditory Output Device Characteristics | Recommended
1.3.1.1 | Video Explanation | Technician’s Toolkit | Recommended
1.3.1.2 | Check Your Understanding | Technician’s Toolkit | Recommended
1.3.2.1 | Video Demonstration | Computer Disassembly | Recommended
1.3.2.2 | Lab | Disassemble a computer | Recommended
Notes: 6

## Slide 7: Chapter 1: Assessment
Students should complete Chapter 1, “Assessment” after completing Chapter 1.
Quizzes, the lab, and other activities can be used to informally assess student progress.
Notes: 7

## Slide 8: Chapter 1: Best Practices
Prior to teaching Chapter 1, the instructor should:
Complete Chapter 1, “Assessment.”
The objectives of this chapter are:
  Explain how to keep personal computer components safe.
  Explain the features and functions of computer components.
  Disassemble a PC.
This chapter includes lectures and concepts. Try to include as many questions as possible to keep students engaged during the presentation.
Notes: 8

## Slide 9: Chapter 1: Best Practices (Cont.)
Section 1.1
  Ask the students or have a class discussion regarding
    What kind of personal computer do they have?
    What are the differences between a desktop PC and a laptop?
    What are different considerations in terms of computing device safety, for example, desktop vs. laptop?
Section 1.2
  Ask the students or have a class discussion
    What are the hardware components in their desktop PC or laptop?
      What is the specification of those components?
      How do specifications affect the performance or functions of the PC or laptop?
      What are new input/output devices that they would like to have? Why?
Notes: 9

## Slide 10: Chapter 1: Best Practices (Cont.)
Section 1.2 (Cont.)
    Pass some components around if you have them while you are discussing or they mention.
    Show pictures of components you put in a PPT or just have files for and have the students tell you what the part is.
    Pass cables around if you have them or show pictures of them if you do not and ask the students what device would connect to that type of cable.
Section 1.3
  Ask the students or have a class discussion
    Have they disassembled or assembled a desktop PC?
    Have they replaced a component on a laptop?
  If there is time, consider playing the video of the computer disassembly provided in the curriculum or another video if computers are not available to disassemble.
Notes: 10

## Slide 11: Chapter 1: Additional Help
For additional help with teaching strategies, including lesson plans, analogies for difficult concepts, and discussion topics, visit the ITE Community at: https://community.cisco.com/t5/networking-academy/ct-p/Netacad, or simply go to https://community.cisco.com
If you have lesson plans or resources that you would like to share, upload them to the ITE Community in order to help other instructors.
Notes: 11

## Slide 12: Chapter 1: Introduction to Personal Computer Hardware
IT Essentials 7.0
Notes: Cisco Networking Academy Program
IT Essentials 7.0
Chapter 1: Introduction to Personal Computer Hardware

## Slide 13: Chapter 1 - Sections & Objectives
1.1 Personal Computers
  Explain how to keep personal computer components safe.
  Explain components in a computer.
  Explain electrical and ESD safety.
1.2 PC Components
  Explain the features and functions of computer components.
  Describe cases and power supplies.
  Describe motherboards.
  Describe CPUs.
  Explain types of memory.
  Describe adapter cards and expansion slots.
  Describe hard disk drives and SSDs.
Notes: 13
Cisco Networking Academy Program
IT Essentials 7.0
Chapter 1: Introduction to Personal Computer Hardware

## Slide 14: Chapter 1 - Sections & Objectives (Cont.)
1.2 PC Components (Cont.)
  Describe optical storage devices.
  Describe ports, cables and adapters.
  Describe input devices.
  Describe output devices.
1.3 Disassemble a PC
  Explain the features and functions of each component in the tool kit.
  Disassemble a computer.
Notes: 14
Cisco Networking Academy Program
IT Essentials 7.0
Chapter 1: Introduction to Personal Computer Hardware

## Slide 15: 1.1 Personal Computer
Notes: 1 – Introduction to Personal Computer Hardware
1.1 – Personal Computer Safety

## Slide 16: Video Explanation – What is in a computer?
Notes: 1 – Introduction to Personal Computer Hardware
1.1 – Personal Computer Safety
1.1.1 – What is in a computer?
1.1.1.1 – Video Explanation - What is in a computer?

## Slide 17: Personal Computers Electrical Safety
Electrical devices have certain power requirements.
AC adapters are manufactured for specific laptops.
  Exchanging AC adapters with a different type of laptop or device may cause damage to both the AC adapter and the laptop.
Some printer parts, such as power supplies, contain high voltage. Check the printer manual for the location of high-voltage components.
Follow electrical safety guidelines to prevent electrical fires, injuries, and fatalities.
Notes: 1 – Introduction to Personal Computer Hardware
1.1 – Personal Computer
1.1.2 – Electrical and ESD Safety
1.1.2.1 – Electrical Safety

## Slide 18: Electrical and ESD Safety ESD
Electrostatic discharge (ESD) can occur when there is a buildup of an electric charge that exists on a surface which comes into contact with another differently charged surface.
ESD can cause damage to computer equipment if not discharged properly.
At least 3,000 volts of static electricity must build up before a person can feel ESD.
Follow these recommendations to help prevent ESD damage:
Keep all components in antistatic bags until you are ready to install them.
Use grounded mats on workbenches.
Use grounded floor mats in work areas.
Use antistatic wrist straps when working inside computers.
Notes: 1 – Introduction to Personal Computer Hardware
1.1 – Personal Computer
1.1.2 – Electrical and ESD Safety
1.1.2.2 – ESD
1.1.2.3 – Check Your Understanding – ESD Characteristics

## Slide 19: 1.2 PC Components
Notes: 1 – Introduction to Personal Computers
1.2 – PC Components

## Slide 20: PC Components Cases
The case houses the internal components such as the power supply, motherboard, central processing unit (CPU), memory, disk drives, and assorted adapter cards.
The term form factor refers to the physical design and look of a case. Common desktop computers are available in form factors including:
Horizontal case
Full-Size Tower
Compact Tower
All-in-one
Many case manufacturers may have their own naming conventions, including super tower, full tower, mid tower, mini tower, cube case, and more.
Notes: 1 – Introduction to Personal Computer Hardware
1.2 – PC Components
1.2.1 – Case and Power Supplies
1.2.1.1 – Cases

## Slide 21: PC Components Power Supplies
Computers use a power supply to convert AC power into a lower voltage DC power required by internal components.
Desktop computer power supply form factors include:
Advanced Technology (AT) – original power supply for legacy computer systems
AT Extended (ATX) – updated version of the AT
ATX12V – the most common power supply on the market today
EPS12V – originally designed for network servers but is now commonly used in high-end desktop models.
Notes: 1 – Introduction to Personal Computer Hardware
1.2 – PC Components
1.2.1 – Case and Power Supplies
1.2.1.2 – Power Supplies

## Slide 22: PC Components Connectors
A power supply includes several different connectors. They are used to power various internal components such as the motherboard and disk drives.
Some examples are:
  20-pin or 24-pin slotted connector
  SATA keyed connector
  Molex keyed connector
  Berg keyed connector
  4-pin to 8-pin auxiliary power connector
  6/8-pin PCIe power connector
Notes: 1 – Introduction to Personal Computer Hardware
1.2 – PC Components
1.2.1 – Case and Power Supplies
1.2.1.3 – Connectors

## Slide 23: PC Components Power Supply Voltage
The different connectors in a power supply also provide different voltages.
The most common voltages supplied are 3.3 volts, 5 volts, and 12 volts.
The 3.3 volt and 5 volt supplies are typically used by digital circuits, while the 12 volt supply is used to run motors in disk drives and fans.
Power supplies can also be single rail, dual rail, or multi rail.
A rail is the printed circuit board (PCB) inside the power supply to which the external cables are connected.
A computer can tolerate slight fluctuations in power, but a significant deviation can cause the power supply to fail.
Notes: 1 – Introduction to Personal Computer Hardware
1.2 – PC Components
1.2.1 – Case and Power Supplies
1.2.1.4 – Power Supply Voltage
1.2.1.5 – Check Your Understanding - Cases and Power Supplies

## Slide 24: PC Components Motherboards
The motherboard is the backbone of the computer.
It is a printed circuit board (PCB) that contains buses, or electrical pathways, that interconnect electronic components.
These components may be soldered directly to the motherboard, or added using sockets, expansion slots, and ports.
Notes: 1 – Introduction to Personal Computer Hardware
1.2 – PC Components
1.2.2 – Motherboards
1.2.2.1 – Motherboards

## Slide 25: PC Components Motherboard Components
Major components on a motherboard include:
  Central Processing Unit (CPU)
  Random Access Memory (RAM)
  Expansion slots
  Chipset
  Basic input/output system (BIOS) chip and Unified Extensible Firmware Interface (UEFI) chip
  SATA connectors
  Internal USB connector
Notes: 1 – Introduction to Personal Computer Hardware
1.2 – PC Components
1.2.2 – Motherboards
1.2.2.2 – Motherboard Components

## Slide 26: PC Components Motherboard Chipset
Chipset consists of the integrated circuits on the motherboard that control how system hardware interacts with the CPU and motherboard.
Most chipsets consist of the following two types:
  Northbridge – Controls high speed access to the RAM and video card.
  Southbridge – Allows the CPU to communicate with slower speed devices including hard drives, Universal Serial Bus (USB) ports, and expansion slots.
Notes: 1 – Introduction to Personal Computer Hardware
1.2 – PC Components
1.2.2 – Motherboards
1.2.2.3 – Motherboard Chipset

## Slide 27: PC Components Motherboard Form Factors
The form factor of motherboards pertains to the size and shape of the board.
There are three common motherboard form factors: Advanced Technology eXtended (ATX), Micro-ATX, and ITX.
The choice of motherboard form factor determines how individual components attach to it, the type of power supply required, and the shape of the computer case.
Notes: 1 – Introduction to Personal Computer Hardware
1.2 – PC Components
1.2.2 – Motherboards
1.2.2.4 – Motherboard Form Factors
1.2.2.5 – Check Your Understanding - Motherboards

## Slide 28: PC Components What is CPU?
The central processing unit (CPU) is responsible for interpreting and executing commands.
The CPU is a small microchip that resides within a CPU package.
The CPU socket is the connection between the motherboard and the processor.
Modern CPU sockets and processor packages are built in following architectures:
  Pin Grid Array (PGA) - the pins are on the underside of the processor package and is inserted into the motherboard CPU socket.
  Land Grid Array (LGA) - the pins are in the socket instead of on the processor.
Notes: 1 – Introduction to Personal Computer Hardware
1.2 – PC Components
1.2.3 – CPU and Cooling Systems
1.2.3.1 – What is CPU?

## Slide 29: PC Components Cooling Systems
Computer components perform better when kept cool.
Computers are kept cool using active and passive cooling solutions.
Active solutions require power while passive solutions do not.
Passive solutions for cooling usually involve reducing the speed at which a component is operating or adding heat sinks to computer chips.
A case fan is considered as active cooling.
Notes: 1 – Introduction to Personal Computer Hardware
1.2 – PC Components
1.2.3 – CPU and Cooling Systems
1.2.3.2 – Cooling Systems
1.2.3.3 – Check Your Understanding - CPUs and Cooling Systems

## Slide 30: PC Components Types of Memory
A computer might use different types of memory chips.
All memory chips store data in the form of bytes.
  A byte is a block of eight bits stored as either 0 or 1 in the memory chip.
Read-Only Memory (ROM) – such as ROM chip.
Random Access Memory (RAM) is the temporary working storage for data and programs that are being accessed by the CPU. RAM is volatile memory.
Adding more RAM in a computer enhances the system performance. However, the maximum amount of RAM that can be installed is limited by the motherboard.
Notes: 1 – Introduction to Personal Computer Hardware
1.2 – PC Components
1.2.4 – Memory
1.2.4.1 – Types of Memory

## Slide 31: PC Components Types of ROM
Types of Read-only Memory (ROM) include:
  ROM chips.
  PROM chips.
  EPROM chips
  EEPROM chips.
Notes: 1 – Introduction to Personal Computer Hardware
1.2 – PC Components
1.2.4 – Memory
1.2.4.2 – Types of ROM

## Slide 32: PC Components Types of RAM
Types of Random Access Memory (RAM) include:
  Dynamic RAM (DRAM)
  Static RAM (SRAM)
  Synchronous Dynamic RAM (SDRAM)
  Double Data Rate Synchronous Dynamic RAM (DDR SDRAM)
  DDR2 Synchronous Dynamic RAM (DDR2 SDRAM)
  DDR3 Synchronous Dynamic RAM (DDR3 SDRAM)
  DDR4 Synchronous Dynamic RAM (DDR4 SDRAM)
  GDDR Synchronous Dynamic RAM (GDDR SDRAM)
Notes: 1 – Introduction to Personal Computer Hardware
1.2 – PC Components
1.2.4 – Memory
1.2.4.3 – Types of RAM

## Slide 33: PC Components Memory Modules
Memory chips are soldered to a circuit board to create a memory module which is placed into a memory slot on the motherboard.
Different types of memory modules include: DIP, SIMM, DIMM memory, and SODIMM.
The speed of memory has a direct impact on how much data a processor can process in a given period of time.
The fastest memory is typically static RAM (SRAM) which is used as cache memory
Notes: 1 – Introduction to Personal Computer Hardware
1.2 – PC Components
1.2.4 – Memory
1.2.4.4 – Memory Modules
1.2.4.5 – Check Your Understanding - Memory

## Slide 34: PC Components Memory Modules (Cont.)
The speed of memory has a direct impact on how much data a processor can process in a given period of time.
The fastest memory is typically static RAM (SRAM) which is used as cache memory for storing the most recently used data and instructions by the CPU.
The three most common types of cache memory are:
  L1 cache – integrated into the CPU
  L2 cache – was original mounted on the motherboard, but now integrated into the CPU
  L3 cache – used some high-end workstations and server CPUs
Notes: 1 – Introduction to Personal Computer Hardware
1.2 – PC Components
1.2.4 – Memory
1.2.4.4 – Memory Modules
1.2.4.5 – Check Your Understanding - Memory

## Slide 35: PC Components Memory Modules (Cont.)
Memory errors occur when the data is not stored correctly in the memory chips. The computer uses different methods to detect and correct data errors in memory.
Different types of error checking methods include:
  Nonparity – Nonparity memory does not check errors in memory.
  Parity – Parity memory contains 8 bits for data and 1 bit for error checking.
  ECC – Error Correction Code memory can detect multiple bit errors in memory and correct single bit errors in memory
Notes: 1 – Introduction to Personal Computer Hardware
1.2 – PC Components
1.2.4 – Memory
1.2.4.4 – Memory Modules
1.2.4.5 – Check Your Understanding - Memory

## Slide 36: PC Components Adapter Cards
Adapter cards increase the functionality of a computer by adding controllers for specific devices or by replacing malfunctioning ports.
Common adapter cards include:
  Sound adapter
  Network Interface Card (NIC)
  Wireless NIC
  Video adapter or display adapter
  Capture card
  TV tuner card
  Universal Serial Bus (USB) controller card
  eSATA card
Notes: 1 – Introduction to Personal Computer Hardware
1.2 – PC Components
1.2.5 – Adapter Cards and Expansion Slots
1.2.5.1 – Adapter Cards and Expansion Slots
1.2.5.2 – Check Your Understanding - Adapter Cards and Expansion Slots

## Slide 37: PC Components Adapter Cards (Cont.)
Computers have expansion slots on the motherboard to install adapter cards.
The type of adapter card connector must match the expansion slot.
Common expansion slots include:
  Peripheral Component Interconnect (PCI)
  Mini-PCI
  PCI eXtended (PCI-X)
  PCI Express (PCIe)
  Riser card
  Accelerated Graphics Port (AGP)
Notes: 1 – Introduction to Personal Computer Hardware
1.2 – PC Components
1.2.5 – Adapter Cards and Expansion Slots
1.2.5.1 – Adapter Cards
1.2.5.2 – Check Your Understanding - Adapter Cards and Expansion Slots

## Slide 38: PC Components Types of Storage Devices
Data drives provide non-volatile storage of data.
Some drives have fixed media, and other drives have removable media.
Data storage devices can be classified according to the media on which the data is stored:
  Magnetic – like hard disk drive and tape drive
  Solid state – like solid state drive
  Optical – like CD and DVD
Notes: 1 – Introduction to Personal Computer Hardware
1.2 – PC Components
1.2.6 – Hard Disk Drives and SSDs
1.2.6.1 – Types of Storage Devices

## Slide 39: PC Components Storage Device Interfaces
Storage devices inside a computer connect to the motherboard using Serial AT Attachment (SATA) connections. The legacy interface is Parallel ATA (EIDE).
The interface standards define the way that data is transferred, the transfer rates, and physical characteristics of the cables and connectors.
There are three main versions of the SATA standard: SATA 1, SATA 2, and SATA 3.
The cables and connectors are the same, but the data transfer speeds are different.
Notes: 1 – Introduction to Personal Computer Hardware
1.2 – PC Components
1.2.6 – Hard Disk Drives and SSDs
1.2.6.2 – Storage Device Interfaces

## Slide 40: PC Components Magnetic Media Storage
This type of storage represents binary values as magnetized or non-magnetized physical areas of magnetic media.
Common types of magnetic media storage drives:
  Hard Disk Drive (HDD) – the traditional magnetic disk devices with storage capacity ranging from gigabytes (GBs) to terabytes (TBs).
  Tape Drive – most often used for archiving data.
    Tape drives use a magnetic read/write head and removable tape cartridge.
    Common tape storage capacities vary between a few GBs to many TBs.
Notes: 1 – Introduction to Personal Computer Hardware
1.2 – PC Components
1.2.6 – Hard Disk Drives and SSDs
1.2.6.3 – Magnetic Media Storage

## Slide 41: PC Components Semiconductor Storage
Solid-state drives (SSD) store data as electrical charges in semiconductor flash memory. This makes SSDs much faster than magnetic HDDs.
SSDs have no moving parts, make no noise, are more energy efficient, and produce less heat than HDDs.
SSDs come in three form factors:
  Disc drive form factor – similar to an HDD
  Expansion cards – plugs directly into the motherboard and mounts in the computer case like other expansion cards
  mSata or M.2 modules – these packages may use a special socket. M.2 is a standard for computer expansion cards.
Notes: 1 – Introduction to Personal Computer Hardware
1.2 – PC Components
1.2.6 – Hard Disk Drives and SSDs
1.2.6.4 – Semiconductor Storage
1.2.6.5 – Check Your Understanding - Data Storage Devices

## Slide 42: PC Components Semiconductor Storage (Cont.)
The Non-Volatile Memory Express (NVMe) specification was developed specifically to allow computers to take greater advantage of the features of SSDs by providing a standard interface between SSDs, the PCIe bus, and operating systems.
NVMe allows compliant SSD drives to attach to the PCIe bus without requiring special drivers.
Solid State Hybrid Drives (SSHDs) are a compromise between a magnetic HDD and an SSD.
  They are faster than an HDD but less expensive than an SSD.
  They combine a magnetic HDD with onboard flash memory serving as a non-volatile cache.
Notes: 1 – Introduction to Personal Computer Hardware
1.2 – PC Components
1.2.6 – Hard disk drives and SSDs
1.2.6.4 – Semiconductor Storage
1.2.6.5 – Check Your Understanding - Data Storage Devices

## Slide 43: PC Components Types of Optical Storage Devices
Optical drives are removable media storage devices that use lasers to read and write data on optical media.
They were developed to overcome the storage capacity limitations of removable magnetic media such as floppy discs.
There are three types of optical drives:
  Compact Disc (CD) - audio and data
  Digital Versatile Disc (DVD) - digital video and data
  Blu-ray Disc (BD) - HD digital video and data
Notes: 1 – Introduction to Personal Computer Hardware
1.2 – PC Components
1.2.7 – Optical Storage Devices
1.2.7.1 – Types of Optical Storage Devices
1.2.7.2 – Check Your Understanding - Types of Optical Storage Devices

## Slide 44: PC Components Types of Optical Storage Devices (Cont.)
CD, DVD, and BD media can be pre-recorded (read only), recordable (write once), or re-recordable (read and write multiple times).
DVD and BD media can also be single layer (SL) or dual layer (DL). Dual layer media roughly doubles the capacity of a single disc.
Notes: 1 – Introduction to Personal Computer Hardware
1.2 – PC Components
1.2.7 – Optical Storage Devices
1.2.7.1 – Types of Optical Storage Devices
1.2.7.2 – Check Your Understanding - Types of Optical Storage Devices

## Slide 45: PC Components Video Ports and Cables
A video port connects a monitor to a computer using a cable.
Video ports and monitor cables transfer analog signals, digital signals, or both.
Video ports and cables include:
  Digital Visual Interface (DVI)
  DisplayPort
  High-Definition Multimedia Interface (HDMI)
  Thunderbolt 1 or 2
  Thunderbolt 3
  Video Graphics Array (VGA)
  Radio Corporation of America (RCA)
Notes: 1 – Introduction to Personal Computer Hardware
1.2 – PC Components
1.2.8 – Ports, Cables, and Adapters
1.2.8.1 – Video Ports and Cables

## Slide 46: PC Components Other Ports and Cables
Input/output (I/O) ports on a computer connect peripheral devices, such as printers, scanners, and portable drives.
A computer may have other ports:
  Personal System 2 (PS/2)
  Audio and game port
  Network
  Serial AT Attachment (SATA)
  Integrated Drive Electronics (IDE)
  The Universal Serial Bus (USB)
Notes: 1 – Introduction to Personal Computer Hardware
1.2 – PC Components
1.2.8 – Ports, Cables, and Adaptors
1.2.8.2 – Other Ports and Cables

## Slide 47: PC Components Adapters and Converters
There are many connection standards in use today. These components are called adapters and converters:
  Converter – performing the same function as an adapter but also translates the signals from one technology to the other.
  Adapter – physically connecting one technology to another
Example of adapters include:
  DVI to VGA Adapter
  USB to Ethernet adapter
  USB to PS/2 adapter
  DVI to HDMI adapter
  Molex to SATA adapter
  HDMI to VGA converter
Notes: 1 – Introduction to Personal Computer Hardware
1.2 – PC Components
1.2.8 – Ports, Cables, and Adaptors
1.2.8.3 – Adapters and Converters
1.2.8.4 – Check Your Understanding - Cables and Connectors

## Slide 48: PC Components The Original Input Devices
Input devices all the user to communicate with a computer.
Some of the first input devices include:
  Keyboard and Mouse – these are the two most commonly used input devices
  ADF / Flatbed Scanner – these devices digitize an image or document
  Joystick and Gamepad – these devices are used for playing games
  KVM Switch – a hardware device that can be used to control more than one computer while using a single keyboard, monitor, and mouse
Notes: 1 – Introduction to Personal Computer Hardware
1.2 – PC Components
1.2.9 – Input Devices
1.2.9.1 – The Original Input Devices

## Slide 49: PC Components New Input Devices
Some new input devices include touch screen, stylus, magnetic strip reader, and barcode scanner:
  Touch screen – input devices with touch or pressure sensitive screens
  Stylus – a type of digitizer that allows a designer or artist to create artwork by using a pen-like tool
  Magnetic strip reader – a device that reads information magnetically encoded on the back of plastic cards
  Barcode scanner – a device that reads the information contained in the barcodes affixed to products
Notes: 1 – Introduction to Personal Computer Hardware
1.2 – PC Components
1.2.9 – Input Devices
1.2.9.2 – New Input Devices

## Slide 50: PC Components More New Input Devices
A few newer input devices:
  Digital camera – devices that capture digital images and videos
  Webcams – video cameras that can be integrated into a computer
  Signature pad– a device that electronically captures a person’s signature
  Smart card reader – a device used on a computer to authenticate the user. A smart card may be the size of a credit card with an embedded microprocessor that is typically under a gold contact pad on one side of the card.
  Microphone – a device that allows a user to speak into a computer and have their voice digitized
Notes: 1 – Introduction to Personal Computer Hardware
1.2 – PC Components
1.2.9 – Input Devices
1.2.9.3 – More New Input Devices

## Slide 51: PC Components Most Recent Input Devices
The newest input devices include NFC devices and terminals, facial recognition scanners, fingerprint scanners, voice recognition scanners, and virtual reality headsets:
  NFC devices and terminals – Near Field Communication (NFC) tap to pay devices
  Facial recognition scanners – devices identifying a user based on unique facial features
  Fingerprint scanners – devices identifying a user based on unique fingerprint
  Voice recognition scanners – devices identifying a user based on unique voice
  Virtual reality headset – used with computer games, simulators, and training applications with virtual reality functionalities.
Notes: 1 – Introduction to Personal Computer Hardware
1.2 – PC Components
1.2.9 – Input Devices
1.2.9.4 – Most Recent Input Devices
1.2.9.5 – Check Your Understanding - Input Devices

## Slide 52: PC Components What are Output Devices?
An output device takes binary information from the computer and converts it into a form that is easily understood by the user.
Examples of output devices include monitors, projectors, VR headsets, printers, speakers, and headphones.
Notes: 1 – Introduction to Personal Computer Hardware
1.2 – PC Components
1.2.10 – Output Devices
1.2.10.1 – What are Output Devices?

## Slide 53: PC Components Monitors and Projectors
Most monitors use one of three types of technology:
  Liquid crystal display (LCD)
  Light-emitting diode (LED)
  Organic LED (OLED)
Most video projectors use LCD or DLP technology.
  DLP stands for Digital Light Processing
  Different projectors have different numbers of lumens, which affects the level of brightness of the projected image.
Notes: 1 – Introduction to Personal Computer Hardware
1.2 – PC Components
1.2.10 – Output Devices
1.2.10.2 – Monitors and Projectors

## Slide 54: PC Components VR and AR Headsets
Virtual Reality (VR) uses computer technology to create a simulated, three-dimensional environment.
A VR headset completely encases the upper portion of users’ faces, not allowing in any ambient light from their surroundings.
Augmented Reality (AR) uses similar technology but superimposes images and audio over the real world in real time.
AR can provide users with immediate access to information about their real surroundings.
An AR headset usually does not close off ambient light to users, allowing them to see their real life surroundings.
Notes: 1 – Introduction to Personal Computer Hardware
1.2 – PC Components
1.2.10 – Output Devices
1.2.10.3 – VR and AR Headsets

## Slide 55: PC Components Printers
Printers are output devices that create hard copies of files.
A hard copy might be a on a sheet of paper. It could also be a plastic form created from a 3D printer.
Different types of printers:
  Inkjet, impact, thermal, laser, and 3D printers
  Printers use wired or wireless connections
  All printers require printing material (such as ink, toner, liquid plastic, etc.)
  Printers use a driver to communicate with OS
Notes: 1 – Introduction to Personal Computer Hardware
1.2 – PC Components
1.2.10 – Output Devices
1.2.10.4 – Printers

## Slide 56: PC Components Speakers and Headphones
Speakers are a type of auditory output device.
Most computers and mobile devices have audio support either integrated into the motherboard or on an adapter card.
Headphones, earbuds, and the earphones found in headsets are all auditory output devices.
These may be wired or wireless. Some are Wi-Fi or Bluetooth-enabled.
Notes: 1 – Introduction to Personal Computer Hardware
1.2 – PC Components
1.2.10 – Output Devices
1.2.10.5 – Speakers and Headphones
1.2.10.6 – Check Your Understanding - Visual and Auditory Output Device Characteristics

## Slide 57: 1.3 Computer Disassembly
Notes: 1 – Introduction to Personal Computers
1.3 – Computer Disassembly

## Slide 58: Video Explanation – Technician's Toolkit
Notes: 1 – Introduction to Personal Computer Hardware
1.3 – Computer Disassembly
1.3.1 – The Technician's Toolkit
1.3.1.1 – Video Explanation - Technician's Toolkit
1.3.1.2 – Check Your Understanding - Technician's Toolkit

## Slide 59: Video Demonstration – Computer Disassembly
Notes: 1 – Introduction to Personal Computer Hardware
1.3 – Computer Disassembly
1.3.2 – Computer Disassembly
1.3.2.1 – Video Demonstration - Computer Disassembly

## Slide 60: Computer Disassembly Lab – Disassemble a Computer
In this lab, you will disassemble a computer using safe lab procedures and the proper tools. Use extreme care and follow all safety procedures. Familiarize yourself with the tools you will be using in this lab.
Note: If you cannot locate or remove the correct component, ask your instructor for help.
Notes: 1 – Introduction to Personal Computer Hardware
1.3 – Computer Disassembly
1.3.2 – Computer Disassembly
1.3.2.2 – Lab - Disassemble a Computer

## Slide 61: 1.4 Chapter Summary
Notes: 1 – Introduction to Personal Computer Hardware
1.4 – Chapter Summary

## Slide 62: Conclusion Chapter 1: Introduction to Personal Computer Hardware
Explain how to keep personal computer components safe.
Explain the features and functions of computer components.
Disassemble a computer.
Notes: 1 – Introduction to Personal Computer Hardware
1.4 – Chapter Summary
1.4.1 – Conclusion

## Slide 63: Chapter 1 New Terms and Commands
Electrostatic discharge (ESD) static electricity antistatic wrist straps alternating current direct current Advanced Technology (AT) AT Extended (ATX) ATX12V EPS12V SATA connector Molex connector Berg connector 4-pin to 8-pin auxiliary power connector | 6/8-pin PCIe power connector printed circuit board (PCB) motherboard Central Processing Unit (CPU) Chipset Serially Attached SCSI (SAS) Northbridge chipset Sorthbridge chipset Universal Serial Bus (USB) Advanced Technology eXtended (ATX) Micro-ATX form factor Mini-ITX form factor ITX form factor Pin Grid Array (PGA) | Land Grid Array (LGA) passive cooling active cooling Random Access Memory (RAM) Dual Inline Package (DIP) Single Inline Memory Module (SIMM) Dual Inline Memory Module (DIMM) Small Outline DIMM (SODIMM) L1 cache L2 cache L3 cache Parity Error Correction Code (ECC) memory
Notes: 1 – Introduction to Personal Computer Hardware
New Terms and Commands

## Slide 64: Chapter 1 New Terms and Commands (Cont.)
Sound adapter Network Interface Card (NIC) Wireless NIC Video adapter or display adapter Capture card TV tuner card Universal Serial Bus (USB) controller card eSATA card Peripheral Component Interconnect (PCI) slot Mini-PCI slot PCI eXtended (PCI-X) slot PCI Express (PCIe) slot | Accelerated Graphics Port (AGP) slot Hard Disk drive Tape drive Solid State drive mSata or M.2 modules Solid State Hybrid Drives (SSHDs) Compact Disc (CD) Digital Versatile Disc (DVD) Blu-ray Disc (BD) DisplayPort Digital Visual Interface (DVI) High-Definition Multimedia Interface (HDMI) | Thunderbolt Video Graphics Array (VGA) Radio Corporation of America (RCA) ADF / Flatbed Scanner Joystick and Gamepad KVM Switch Touch screen Stylus Magnetic strip reader Barcode scanner Signature pad Smart card reader NFC devices and terminals
Notes: 1 – Introduction to Personal Computer Hardware
New Terms and Commands

## Slide 65: Chapter 1 New Terms and Commands (Cont.)
Facial recognition scanners Fingerprint scanners Voice recognition scanners Virtual reality headset Liquid crystal display (LCD) Light-emitting diode (LED) Organic LED (OLED) Digital Light Processing (DLP) Virtual Reality (VR) Augmented Reality (AR) Basic input/output system (BIOS) chip Unified Extensible Firmware Interface (UEFI) chip | Serial Advanced Technology Attachment (SATA) Enhanced Integrated Drive Electronics (EIDE) Small Computer System Interface (SCSI) Read-Only Memory (ROM) Programmable read-only memory chip (PROM) Erasable programmable read-only memory chip (EPROM) Electrically erasable programmable read-only memory chip (EPROM) | Dynamic RAM (DRAM) Static RAM (SRAM) Synchronous Dynamic RAM (SDRAM) Double Data Rate Synchronous Dynamic RAM (DDR SDRAM) DDR2 Synchronous Dynamic RAM (DDR2 SDRAM) DDR3 Synchronous Dynamic RAM (DDR3 SDRAM) DDR4 Synchronous Dynamic RAM (DDR4 SDRAM) GDDR Synchronous Dynamic RAM (GDDR SDRAM)
Notes: 1 – Introduction to Personal Computer Hardware
New Terms and Commands