## Slide 1: Chapter 8: Printers
Instructor Materials
IT Essentials v7.0
Notes: Cisco Networking Academy Program
IT Essentials v7.0
Chapter 8: Printers

## Slide 2: Instructor Materials – Chapter 8 Planning Guide
This PowerPoint deck is divided in two parts:
Instructor Planning Guide
  Information to help you become familiar with the chapter
  Teaching aids
Instructor Class Presentation
  Optional slides that you can use in the classroom
  Begins on slide #13
Note: Remove the Planning Guide from this presentation before sharing with anyone.
Notes: 2

## Slide 3: Chapter 8: Printers
IT Essentials 7.0 Planning Guide
Notes: Cisco Networking Academy Program
IT Essentials v7.0
Chapter 8: Printers

## Slide 4: Check Your Understanding and What Do You Already Know?
Check Your Understanding activities used to be called Interactive Activities. They simply have a new name. They are designed to let students quickly determine if they understand the content and can proceed, or if they need to review.
Check Your Understanding activities do not affect student grades.
Activities listed as What Do You Already Know? are a type of activity in which we ask the student to simply take a guess! It is not meant to evaluate their knowledge. It is only meant to give them a head start in thinking about different topics before they are presented in the course. Students receive addition content in the form of feedback for any answers they select.
What Do You Already Know? activities do not directly affect student grades; however, the feedback may contain content which appears later in quizzes and exams, so it is important that students complete the What Do You Already Know? activities.
Notes: 4

## Slide 5: Chapter 8: Activities
What activities are associated with this chapter?
Page # | Activity Type | Activity Name | Optional?
8.1.1.5 | Check Your Understanding | Printer Capabilities and Characteristics | Recommended
8.1.2.2 | Check Your Understanding | Printer Connections | Recommended
8.2.1.3 | Check Your Understanding | Inkjet Printers | Recommended
8.2.2.3 | Check Your Understanding | Laser Printers | Recommended
8.2.3.2 | Check Your Understanding | The Laser Printing Process | Recommended
8.2.4.3 | Check Your Understanding | Thermal Printers and Impact Printers | Recommended
8.2.5.3 | Check Your Understanding | Virtual Printers | Recommended
8.2.6.3 | Check Your Understanding | 3D Printers | Recommended
8.3.1.2 | Lab | Install a Printer in Windows | Recommended
8.3.2.2 | Check Your Understanding | Configuration Options | Recommended
8.3.3.3 | Check Your Understanding | Printer Optimization (Figure 1) | Recommended
8.3.3.3 | Check Your Understanding | Printer Hardware Optimization (Figure 2) | Recommended
Notes: 5

## Slide 6: Chapter 8: Activities (Cont.)
What activities are associated with this chapter?
Page # | Activity Type | Activity Name | Optional?
8.4.1.3 | Lab | Share a Printer in Windows | Recommended
8.4.2.5 | Check Your Understanding | Print Servers | Recommended
8.5.1.2 | What Do You Already Know | Printer Operating Environment | Recommended
8.5.2.1 | Video Demonstration | Inkjet Printer Preventive Maintenance | Recommended
8.5.2.2 | Lab | Perform Preventive Maintenance on an Inkjet Printer | Recommended
8.5.3.1 | Video Demonstration | Laser Printer Preventive Maintenance | Recommended
8.5.3.2 | Lab | Preventive Maintenance on a Laser Printer | Recommended
8.5.4.2 | Check Your Understanding | Thermal Printer Preventive Maintenance | Recommended
8.5.5.2 | Check Your Understanding | Impact Printer Preventive Maintenance | Recommended
8.5.6.1 | Video Demonstration | 3D Printer Preventive Maintenance | Recommended
8.5.6.2 | Video Demonstration | 3D Printer Printing a Component | Recommended
Notes: 6

## Slide 7: Chapter 8: Assessment
Students should complete Chapter 8, “Assessment” after completing Chapter 8.
Quizzes, labs, and other activities can be used to informally assess student progress.
Notes: 7

## Slide 8: Chapter 8: Best Practices
Prior to teaching Chapter 8, the instructor should:
Complete Chapter 8, “Assessment.”
The objectives of this chapter are:
  Explain the purpose and characteristics of different types of printers.
  Compare different types of printers.
  Install a printer.
  Configure printer sharing.
  Implement preventive maintenance and troubleshooting techniques on printers.
Notes: 8

## Slide 9: Chapter 8: Best Practices (Cont.)
Make sure the students understand the potential safety hazards and safety procedures associated with printers and scanners—high temperature on laser printers, high voltage on laser printers, scanner LEDs.
If there is time, show the videos for any types of printers you don’t have in the classroom or make them mandatory for an online course.
Practice finding printer drivers or printer driver upgrades say for an older printer that is currently installed on a Windows 7 computer that is being upgraded to Windows 10 or demonstrate how you would do this.
Have the students adjust printer settings for collation, duplexing if possible, and orientation.
One way to go through the different printer types is to divide the class into 5 groups (impact, inkjet, thermal, 3D, and laser). Give them time to research information about what makes their type of printer different and present in less than 5 minutes the most important points.
Notes: 9

## Slide 10: Chapter 8: Best Practices (Cont.)
Have students tell of any printer problems they have had and what they did to fix it.
Let the students work in pairs or individually to shop for a printer based on a particular situation. Hand out different scenarios such as a homebound elder needs to print shipping documents for an online handcraft business she runs. She has a computer running Windows 7 Home Basic. What type of printer would you recommend and why? You could also put a price limit on the purchase. If the students do not have Internet access, copy some ads from the Internet and print copies that are passed amongst the students. Give them 2 minutes to describe the situation, what printer they chose, and why they chose that particular type.
Consider playing the video on the 3D printer or another video so they can see it in action.
If you have a printer in the room, consider configuring printer sharing in front of the class to demonstrate the concept.
Notes: 10

## Slide 11: Chapter 8: Additional Help
For additional help with teaching strategies, including lesson plans, analogies for difficult concepts, and discussion topics, visit the ITE Community at: https://community.cisco.com/t5/networking-academy/ct-p/Netacad, or simply go to https://community.cisco.com.
If you have lesson plans or resources that you would like to share, upload them to the ITE Community in order to help other instructors.
Notes: 11

## Slide 12: Chapter 8: Printers
IT Essentials v7.0
Notes: Cisco Networking Academy Program
IT Essentials v7.0
Chapter 8 Printers

## Slide 13: Chapter 8 - Sections & Objectives
8.1 Common Printer Features
  Describe characteristics and capabilities of printers.
  Identify printer connectors and ports.
8.2 Printer Type Comparison
  Explain the parts and characteristics of inkjet printers.
  Explain the parts and characteristics of laser printers.
  Explain how laser printers operate.
  Explain the parts and characteristics of thermal printers and impact printers.
  Explain the characteristics of virtual printers.
  Explain the parts and characteristics of 3D printers.
Notes: 13
Cisco Networking Academy Program
IT Essentials v7.0
Chapter 8: Printers

## Slide 14: Chapter 8 - Sections & Objectives (Cont.)
8.3 Installing and Configuring Printers
  Install and update the device driver, firmware, and RAM for the printer.
  Explain how to configure settings on a printer.
  Explain how to optimize printing performance.
8.4 Sharing Printers
  Explain how to configure printer sharing.
  Configure printer sharing using a print server.
8.5 Maintaining and Troubleshooting Printers
  Explain vendor guidelines and the importance of appropriate operational environments for printers.
  Implement preventive maintenance on an inkjet printer.
Notes: 14
Cisco Networking Academy Program
IT Essentials v7.0
Chapter 8: Printers

## Slide 15: Chapter 8 - Sections & Objectives (Cont.)
8.5 Maintaining and Troubleshooting Printers (cont.)
  Implement preventive maintenance on a laser printer.
  Explain how to perform preventive maintenance on a thermal printer.
  Explain how to perform preventive maintenance on an impact printer.
  Explain how to perform preventive maintenance on a 3D printer.
  Explain the six steps of the troubleshooting printers.
  Describe common problems and solutions for printers.
Notes: 15
Cisco Networking Academy Program
IT Essentials v7.0
Chapter 8: Printers

## Slide 16: 8.1 Common Printer Features
Notes: 8 – Printers
8.1 – Common Printer Features

## Slide 17: Characteristics and Capabilities Characteristics of Printers
Notes: 8.1 – Common Printer Features
8.1.1 – Characteristics and Capabilities
8.1.1.1 – Characteristics of Printers

## Slide 18: Characteristics and Capabilities Printer Speed, Quality, and Color
Speed and Quality
  Speed – measured in pages per minute (ppm)
  Quality – measured in dots per inch (dpi)
Color
  Cyan, magenta, and yellow (CMY)
  Black for inkjets is the base or key color
Notes: 8.1 – Common Printer Features
8.1.1 – Characteristics and Capabilities
8.1.1.2 – Printer Speed, Quality, and Color

## Slide 19: Characteristics and Capabilities Reliability and Total Cost of Ownership
Warranty
Scheduled servicing
Mean time between failures (MTBF)
Total cost of ownership (TCO)
  Initial purchase price
  Cost of consumable supplies
  Price per page
  Pages per month
  Maintenance costs
  Warranty costs
Notes: 8.1 – Common Printer Features
8.1.1 – Characteristics and Capabilities
8.1.1.3 – Reliability and Total Cost of Ownership

## Slide 20: Characteristics and Capabilities Automatic Document Feeder
Automatic Document Feeder (ADF)
  Used with some laser and inkjet models
  Feeds paper into the printer
  Might provide collation (ordering of pages)
Notes: 8.1 – Common Printer Features
8.1.1 – Characteristics and Capabilities
8.1.1.4 – Automatic Document Feeder
8.1.1.5 – Check Your Understanding – Printer Capabilities and Characteristics

## Slide 21: 8.2 Printer Type Comparison
Notes: 8 – Printers
8.2 – Printer Type Comparison

## Slide 22: Inkjet Printers Inkjet Printer Characteristics
Easy to use
Cheaper than laser printers
Advantages
  Low cost
  High resolution
Disadvantages
  Some nozzles prone to clog
  Cartridges can be expensive
  Ink can be wet after printing
Notes: 8.2 – Printer Type Comparison
8.2.1 – Inkjet Printers
8.2.1.1 – Inkjet Printer Characteristics

## Slide 23: Inkjet Printers Inkjet Printer Parts
Ink Cartridge/ Paper
Feeder
Duplexing Assembly
Print Head
Carriage/Belt
Roller
Notes: 8.2 – Printer Type Comparison
8.2.1 – Inkjet Printers
8.2.1.2 – Inkjet Printer Parts
8.2.1.3 – Check Your Understanding – Inkjet Printers

## Slide 24: Laser Printers Laser Printer Characteristics
Advantages
  Low cost per page
  High PPM
  High capacity
  High quality
  Fast (uses a laser beam or LEDs to create an image)
  Print comes out dry
Disadvantages
  High initial cost
  Toner cartridges can be expensive
Notes: 8.2 – Printer Type Comparison
8.2.2 – Laser Printers
8.2.2.1 – Laser Printer Characteristics

## Slide 25: Laser Printers Laser Printer Characteristics
Duplexing Assembly
Fuser Assembly
Toner Cartridge
Pickup Rollers
Transfer Roller
Imaging Drum
Notes: 8.2 – Printer Type Comparison
8.2.2 – Laser Printers
8.2.2.2 – Laser Printer Characteristics
8.2.2.3 – Check Your Understanding – Laser Printers

## Slide 26: Laser Printing Process How Laser Printing Works
7 Steps of the Laser Printing Process
Processing – Convert data into a printable form
Charging – drum is conditioned for new image
Exposing – write the image to the drum using a laser beam
Developing – toner is applied to the image on the drum
Transferring – As the paper rolls through, the image is transferred to the paper due to a charge applied to the paper
Fusing – Heat and pressure are applied to the paper
Cleaning – Excess toner removed from the drum
Notes: 8.2 – Printer Type Comparison
8.2.3 – Laser Printing Process
8.2.3.1 – How Laser Printing Works
8.2.3.2 – Check Your Understanding – The Laser Printing Process

## Slide 27: Thermal Printers and Impact Printers Thermal Printer Characteristics
Thermal printers are used in retail as part of a cash register system and within older fax machines.
Heat from the print head makes the image on the paper.
Advantages
  Last a long time due to few moving parts
  Quiet
  No cost for ink or toner
Disadvantages
  Thermal paper is expensive and must be stored at room temperature
  Images on thermal paper degrade over time, are poor quality, and cannot be in color
Notes: 8.2 – Printer Type Comparison
8.2.4– Thermal Printers and Impact Printers
8.2.4.1 – Thermal Printer Characteristics

## Slide 28: Thermal Printers and Impact Printers Impact Printer Characteristics
Impact printers – dot matrix and daisy wheel
Have print heads that strike an inked ribbon with a specific number of pins
  Higher number of pins means better quality
Advantages
  Ribbons are less expensive supplies than other types
  Can use regular paper or continuous feed paper
  Can print carbon copies
Disadvantages
  Noisy
  Graphics are low-resolution
  Limited color capabilities
Notes: 8.2 – Printer Type Comparison
8.2.4– Thermal Printers and Impact Printers
8.2.4.2 – Impact Printer Characteristics
8.2.4.3 Check Your Understanding – Thermal Printers and Impact Printers

## Slide 29: Virtual Printers Virtual Printer Characteristics
Print to file
Print to PDF
Print to XPS (XML Paper Specification)
Print to image (such as .JPG or .TIF)
Notes: 8.2 – Printer Type Comparison
8.2.5– Virtual Printers
8.2.5.1 – Virtual Printer Characteristics

## Slide 30: Virtual Printers Cloud Printing
Sends a print job to a remote printer somewhere on the network.
Some printing companies have software that can send print jobs to their closest location.
Google Cloud Print allows you to connect your printer to the web and you can send something to your own printer no matter where you are located.
Notes: 8.2 – Printer Type Comparison
8.2.5– Virtual Printers
8.2.5.2 – Cloud Printing
8.2.5.3 Check Your Understanding – Virtual Printers

## Slide 31: 3D Printers 3D Printer Characteristics
Used to create three dimensional objects
Use plastic filament or other media to create the object
Notes: 8.2 – Printer Type Comparison
8.2.6 – 3D Printers
8.2.6.1 – 3D Printer Characteristics

## Slide 32: 3D Printers 3D Printer Parts
Print Bed
Hotend Nozzle
Axis
Feeder
Filament
Notes: 8.2 – Printer Type Comparison
8.2.6 – 3D Printers
8.2.6.2 – 3D Printer Parts
8.2.6.3 – Check Your Understanding – 3D Printers

## Slide 33: 8.3 Installing and Configuring Printers
Notes: 8 – Printers
8.3 – Installing and Configuring Printers

## Slide 34: Installing and Updating a Printer Installing a Printer
Follow manufacturer’s instructions.
Remove all packing material and keep if a return is needed.
Sometimes the printer driver is installed before the printer is connected to the computer.
Connect the cable to the printer and computer or connect the network cable.
Attach power cord.
Notes: 8.3 – Installing and Configuring Printers
8.3.1– Installing and Updating a Printer
8.3.1.1 – Installing a Printer

## Slide 35: Installing and Updating a Printer Lab - Install a Printer
In this lab, you will install a printer. You will find, download, and update the driver and the software for the printer.
Notes: 8.3 – Installing and Configuring Printers
8.3.1– Installing and Updating a Printer
8.3.1.2 – Lab - Install a Printer

## Slide 36: Installing and Updating a Printer Test Printer Functions
Test all functions including
  Double-sided documents
  Different paper trays
  Grayscale and color
  Draft mode
  Collation
Notes: 8.3 – Installing and Configuring Printers
8.3.1– Installing and Updating a Printer
8.3.1.3 – Test Printer Functions

## Slide 37: Configuring Options and Default Settings Common Configuration Settings
Notes: 8.3 – Installing and Configuring Printers
8.3.2– Configuring Options and Default Settings
8.3.2.1 – Common Configuration Settings
8.3.2.2 – Check Your Understanding – Configuration Options

## Slide 38: Optimizing Printer Performance Software Optimization
Use the print driver software to
  Configure print spool settings
  Calibrate the printer (color)
  Set paper orientation
Notes: 8.3 – Installing and Configuring Printers
8.3.3– Optimizing Printer Performance
8.3.3.1 – Software Optimization

## Slide 39: Optimizing Printer Performance Hardware Optimization
Firmware
Printer memory
Notes: 8.3 – Installing and Configuring Printers
8.3.3– Optimizing Printer Performance
8.3.3.2 – Hardware Optimization
8.3.3.3 – Check Your Understanding – Printer Optimization (Figure 1) and Printer Hardware Optimization (Figure 2)

## Slide 40: 8.4 Sharing Printers
Notes: 8 – Printers
8.4 – Sharing Printers

## Slide 41: Operating System Settings for Sharing Printers Configuring Printer Sharing
Those who connect to the shared printer must have the correct print driver.
  Windows can do this automatically
Notes: 8.4 – Sharing Printers
8.4.1– Operating System Settings for Sharing Printers
8.4.1.1 – Configuring Printer Sharing

## Slide 42: Operating System Settings for Sharing Printers Wireless Printer Connections
Bluetooth
  Pairing between computer and printer
Wi-Fi
Notes: 8.4 – Sharing Printers
8.4.1– Operating System Settings for Sharing Printers
8.4.1.2 – Wireless Printer Connections

## Slide 43: Operating System Settings for Sharing Printers Lab – Share a Printer in Windows
In this lab, you will share a printer, configure the printer on a networked computer, and print a test page from the remote computer.
Notes: 8.4 – Sharing Printers
8.4.1– Operating System Settings for Sharing Printers
8.4.1.3 – Lab – Share a Printer in Windows

## Slide 44: Print Servers Purposes of Print Servers
Provide client access to print resources
Administrate print jobs by storing them in a queue
Provide user feedback
Notes: 8.4 – Sharing Printers
8.4.2– Print Servers
8.4.2.1 – Purposes of Print Servers

## Slide 45: Print Servers Software Print Servers
Use print server software.
Disadvantages
  Sharing a printer might cause slow downs.
  If the computer sharing the printer is down, the printer is unavailable to others.
Notes: 8.4 – Sharing Printers
8.4.2– Print Servers
8.4.2.2 – Software Print Servers

## Slide 46: Print Servers Hardware Print Servers
Notes: 8.4 – Sharing Printers
8.4.2– Print Servers
8.4.2.3 – Hardware Print Servers

## Slide 47: Print Servers Dedicated Print Servers
Powerful processor
Adequate storage space for queued documents
Adequate memory
Notes: 8.4 – Sharing Printers
8.4.2– Print Servers
8.4.2.4 – Dedicated Print Servers
8.4.2.5 – Check Your Understanding – Print Servers

## Slide 48: 8.5 Maintaining and Troubleshooting Printers
Notes: 8 – Printers
8.5 – Troubleshooting and Maintaining Printers

## Slide 49: Printer Preventive Maintenance Vendor Guidelines
Refer to the printer’s documentation.
Follow recommended maintenance processes and instructions.
Some manufacturers sell maintenance kits.
Notes: 8.5 – Maintaining and Troubleshooting Printers
8.5.1– Printer Preventive Maintenance
8.5.1.1 – Vendor Guidelines
8.5.1.2 – What Do You Already Know? Printer Operating Environment

## Slide 50: Inkjet Printer Preventive Maintenance Video Demonstration – Inkjet Printer Preventive Maintenance
Notes: 8.5 – Maintaining and Troubleshooting Printers
8.5.2– Inkjet Printer Preventive Maintenance
8.5.2.1 – Video Demonstration – Inkjet Printer Preventive Maintenance

## Slide 51: Inkjet Printer Preventive Maintenance Lab – Perform Preventive Maintenance on an Inkjet Printer
In this lab, you will perform preventive maintenance on an inkjet printer. Note: The lab instructions are for general reference only. Refer to the manufacturer’s printer manual for instructions to perform preventive maintenance on your inkjet printer model.
Notes: 8.5 – Maintaining and Troubleshooting Printers
8.5.2– Inkjet Printer Preventive Maintenance
8.5.2.2 – Lab – Perform Preventive Maintenance on an Inkjet Printer

## Slide 52: Laser Printer Preventive Maintenance Video Demonstration – Laser Printer Preventive Maintenance
Notes: 8.5 – Maintaining and Troubleshooting Printers
8.5.3– Laser Printer Preventive Maintenance
8.5.3.1 – Video Demonstration – Laser Printer Preventive Maintenance

## Slide 53: Laser Printer Preventive Maintenance Lab – Perform Preventive Maintenance on a Laser Printer
In this lab, you will perform preventive maintenance on a laser printer.
Note: The lab instructions are for general reference only. Refer to the manufacturer’s printer manual for instructions to perform preventive maintenance on your laser printer model.
Notes: 8.5 – Maintaining and Troubleshooting Printers
8.5.3– Laser Printer Preventive Maintenance
8.5.3.2 – Lab – Perform Preventive Maintenance on a Laser Printer

## Slide 54: Thermal Printer Preventive Maintenance Perform Preventive Maintenance on a Thermal Printer
Refer to the printer’s documentation.
Replace the paper.
Clean the heating element with a cotton swab dampened with isopropyl alcohol.
Use compressed air or a ling-free cloth to remove debris.
Notes: 8.5 – Maintaining and Troubleshooting Printers
8.5.4 – Thermal Printer Preventive Maintenance
8.5.4.1 – Perform Preventive Maintenance on a Thermal Printer
8.5.4.2 – Check Your Understanding – Thermal Printer Preventive Maintenance

## Slide 55: Impact Printer Preventive Maintenance Perform Preventive Maintenance on an Impact Printer
Refer to the printer’s documentation.
Replace the ribbon.
Check character quality – might need to replace the print head.
Notes: 8.5 – Maintaining and Troubleshooting Printers
8.5.5– Impact Printer Preventive Maintenance
8.5.5.1 – Perform Preventive Maintenance on an Impact Printer
8.5.5.2 – Check Your Understanding – Impact Printer Preventive Maintenance

## Slide 56: 3D Printer Preventive Maintenance Video Demonstration – 3D Printer Preventive Maintenance
Notes: 8.5 – Maintaining and Troubleshooting Printers
8.5.6– 3D Printer Preventive Maintenance
8.5.6.1 – Video Demonstration – 3D Printer Preventive Maintenance

## Slide 57: 3D Printer Preventive Maintenance Video Demonstration – 3D Printer Printing a Component
Notes: 8.5 – Maintaining and Troubleshooting Printers
8.5.6– 3D Printer Preventive Maintenance
8.5.6.2 – Video Demonstration – 3D Printer Printing a Component
8.5.6.3 – Check Your Understanding – 3D Printer Preventive Maintenance

## Slide 58: Troubleshooting Printing Issues The Six Steps of the Troubleshooting Process
Notes: 8.5 – Maintaining and Troubleshooting Printers
8.5.7– Troubleshooting Printing Issues
8.5.7.1 – The Six Steps of the Troubleshooting Process

## Slide 59: Troubleshooting Printing Issues Identify the Problem
Notes: 8.5 – Maintaining and Troubleshooting Printers
8.5.7– Troubleshooting Printing Issues
8.5.7.2 – Identify the Problem

## Slide 60: Troubleshooting Printing Issues Establish a Theory of Probable Cause
Notes: 8.5 – Maintaining and Troubleshooting Printers
8.5.7– Troubleshooting Printing Issues
8.5.7.3 – Establish a Theory of Probably Cause

## Slide 61: Troubleshooting Printing Issues Test the Theory to Determine Cause
Notes: 8.5 – Maintaining and Troubleshooting Printers
8.5.7– Troubleshooting Printing Issues
8.5.7.4 – Test the Theory to Determine Cause

## Slide 62: Troubleshooting Printing Issues Establish a Plan of Action to Resolve the Problem and Implement the Solution
Notes: 8.5 – Maintaining and Troubleshooting Printers
8.5.7– Troubleshooting Printing Issues
8.5.7.5 – Establish a Plan of Action to Resolve the Problem and Implement the Solution

## Slide 63: Troubleshooting Printing Issues Verify Full System Functionality and, If Applicable, Implement Preventive Measures
Notes: 8.5 – Maintaining and Troubleshooting Printers
8.5.7– Troubleshooting Printing Issues
8.5.7.6 – Verify Full System Functionality and, If Applicable, Implement Preventive Measures

## Slide 64: Troubleshooting Printing Issues Document Findings, Actions, and Outcomes
Notes: 8.5 – Maintaining and Troubleshooting Printers
8.5.7– Troubleshooting Printing Issues
8.5.7.7 – Document Findings, Actions, and Outcomes

## Slide 65: Problems and Solutions Identify Printer Problems and Solutions
Notes: 8.5 – Maintaining and Troubleshooting Printers
8.5.8 – Problems and Solutions
8.5.8.1 – Identify Printer Problems and Solutions

## Slide 66: Problems and Solutions Common Problems and Solutions for Printers
Notes: 8.5 – Maintaining and Troubleshooting Printers
8.5.8 – Problems and Solutions
8.5.8.2 – Common Problems and Solutions for Printers

## Slide 67: Problems and Solutions Common Problems and Solutions for Printers (cont.)
Notes: 8.5 – Maintaining and Troubleshooting Printers
8.5.8 – Problems and Solutions
8.5.8.2 – Common Problems and Solutions for Printers

## Slide 68: 8.6 Chapter Summary
Notes: 8 – Printers
8.6 – Chapter Summary

## Slide 69: Section 8.6 New Terms and Commands
Laser printer Inkjet printer Impact printer Thermal printer 3D printer ADF Print head Roller Feeder Duplexing assembly Ink cartridge Carriage/belt Imaging drum Toner cartridge | Fuser assembly Transfer roller Pickup rollers Processing Charging Exposing Developing Transferring Fusing Cleaning Virtual printer Print to file Print to PDF Print to XPS | Print to image Cloud printing Plastic filament Filament Feeder Hotend Nozzle Axis Print bed Printer driver Collation Hardware print server Software print server Dedicated print server Preventive maintenance
Notes: Chapter 8 - New Terms and Commands