## Slide 1: RIP
Course Code: CSC 3116
Dept. of Computer Science
Faculty of Science and Technology
Lecturer No: | Lab 5 | Week No: | 5 | Semester: | Summer 23-24
Lecturer: | Md. Faruk Abdullah Al Sohan; faruk.sohan@aiub.edu |  |  |  | 
Course Title: Computer Networks

## Slide 2: RIPv2 Configuration
172.16.1.0/30
172.16.1.4/30
192.168.2.0/24
IOS Commands
R1(config)# router rip
R1(config-router)# version 2
R1(config-router)#network 172.16.1.0
R1(config-router)#network 172.16.1.4
R1(config-router)#network 192.168.2.0
R1(config-router)#no auto-summary

## Slide 3: RIPv2 Configuration
Trableshooting
172.16.1.0/30
172.16.1.4/30
192.168.2.0/24
To show protocol properties
  show ip protocols
To show all routes
  show ip route
To show all RIP activities in real-time
  debug ip rip
  To stop debugging
  no debug all
  To show RIP database
  show ip rip database

## Slide 4: Task
IOS Commands
R1(config)# router rip
R1(config-router)# version 2
R1(config-router)#network 172.16.1.0
R1(config-router)#network 172.16.1.4
R1(config-router)#network 192.168.2.0
R1(config-router)#no auto-summary

## Slide 5
References
[1] R. Graziani and A. Johnson, Routing Protocols and Concepts, 2nd ed.,
Cisco Systems, Inc., USA, 2008, pp. 148-173.
[2] J. Macfarlane, Network Routing Basics, Wiley Publications. Inc.,
2006, USA, pp. 70-104.

## Slide 6
Books
  1. Official Cert Guide CCNA 200-301 , vol. 1, W. Odom, Cisco Press, First Edition, 2019, USA.
  2. CCNA Routing and Switching, T. Lammle, John Wily & Sons, Second Edition, 2016, USA.